## Slide 1: Productive Design of Extensible On-Chip Memory Hierarchies
Henry Cook
5/10/2016
Dave Patterson, Krste Asanović

## Slide 2: The end of Moore’s Law?
Dennard Scaling
Tick/Tock broken
Parallelism
Specialization
Design renaissance

## Slide 3: Where’s the energy going?
Caching/Hierarchy
Table of J/ops

## Slide 4: Who’s in charge?
of managing the memory hierarchy

## Slide 5: What is cache coherence?
SWMR
Policy vs Protocol

## Slide 6: Why is cache coherence hard?
Distributed consensus about which agent has what permissions on a cache block
  Permissions changes need to be done correctly and atomically
  Concurrency must be managed in high BW systems
Semantic gap between verifiable specification and concrete implementations

## Slide 7: What can be done?
Language and Tools
  Meta-programming
  Functional programming
  Objects & multiple inheritance
Development Methodology
  Design space exploration
  Generators >> design instances
  Agile & open source

## Slide 8: What does this thesis contribute?
A general framework for context-dependent parameterization of hardware generators.
A set of Chisel libraries for generating extensible cache-coherent memory hierarchies.
A methodology for decomposing high-level descriptions of cache coherence protocols into controller-localized, object-oriented transactions.

## Slide 9: Design Ethos
Productivity
  “The essence of abstractions is preserving information that is relevant in a given context, and forgetting information that is irrelevant in that context.”
      Guttag
Extensibility
  “A successful platform means that building the second thing is easier than building the first.”
      Katz

## Slide 10: Three Interacting Abstractions

## Slide 11: Chapter 3: TileLink

## Slide 12: What is TileLink?
A framework designed to be a substrate for policy transactions
Hierarchical / composable / deadlock-free
Built-in message types (for accelerators)
Extensible with custom message types (for CC)

## Slide 13: Transactional view of cache coherence

## Slide 14: Channels
Acquire
  Initiates a transaction to acquire access to a cache block with the proper permissions.
  Also used to write data without caching it locally.
Probe
  Queries a client to revoke its permissions on a block.
Release
  Acknowledges probe receipt, releasing permissions on the block.
  Also used to voluntarily write back dirty data.
Grant
  Provides data or permissions to the original requestor, granting access to the cache block.
  Also used to acknowledge voluntary Releases.
Finish
  Final acknowledgment of transaction completion from requestor.

## Slide 15: Assumptions and guarantees
Relative channel priorities -> forward progress
Finish messages -> unordered p2p delivery

## Slide 16: Manager-Client Pairing (MCP)

## Slide 17: Supply concrete physical networks

## Slide 18: Chapter 4: CoherencePolicy

## Slide 19: Object orientation in hardware
Objects are abstractions that contain fields of data that are mutated and accessed by procedural methods
  opaque blobs of bits
Encapsulation
  Controller authors don’t need to know the specific format used or the meaning of individual bits
  Policy authors get a set of questions to answer

## Slide 20: Client Metadata
Metadata contains client state, policy determines:
  what permissions apply to each state
  which messages to send in response to mem ops or Probes
  how to change state in response to ops, Probes, Grants
A sample of ClientMetadata’s API:
  isValid()
  isHit(cmd)
  makePrimaryAcquire(id, addr, cmd)
  makeVoluntaryWriteback(id, addr, data)
  makeRelease(probe, id, data)
  onHit(cmd)
  onProbe(probe)
  onGrant(incoming, outstanding)

## Slide 21: ManagerMetadata
Metadata contains manager state and/or sharer tracking information, policy determines:
  what permissions apply to each state
  which messages to send in response to Acquires or Releases
  how to change state and sharers in response to Releases and Grants
A sample of ManagerMetadata’s API:
  requiresProbes(acquire)
  makeProbe(acquire)
  makeProbeForVoluntaryWriteback()
  makeGrant(acquire, id, data)
  onRelease(incoming, source_id)

## Slide 22: HierarchicalMetadata
A single agent can be both a Manager with respect to inner caches and a Client with respect to some outer cache or hub
Has both types of metadata
Uses memory op codes to translate Acquires, Releases and Probes between realms

## Slide 23: Supply concrete directory format

## Slide 24: Chapter 4: Message Flows

## Slide 25: Message flows
Global view of transaction
Used to generate invariants for formal methods

## Slide 26: A writeback flow

## Slide 27: A load miss sub-flow

## Slide 28: A store flow

## Slide 29: Fun!

## Slide 30: From global to local flows

## Slide 31: From local flows to cache controllers
Sub-flows expressed as Scala traits containing
  methods on ports
  scoreboard bits tracking dataflow
Transaction Handling Status Registers (TSHRs)
  combine traits with required functionality
  express any inter-sub-flow dependencies

## Slide 32: Supply concrete agent resources

## Slide 33: Separation of concerns
Notes: A metadata-based policy is not concerned with anything having to do with time or ordering, only with what action needs to be taken when the system is in a particular state. This factoring allows multiple policies to be plugged in without changing controller design or network implementation.
The TileLink framework determines what types of messages any coherence policy methods can possibly output. It is not concerned with which messages should be sent under what conditions, just the relative priority and allowed orderings of the general message types. This factoring allows multiple network implementations to be plugged in without changing controller design or policy contents.
Message flow factoring allows the pipeline implementation of the cache controller logic to be changed without requiring changes to the policy description or network implementation.
Agent implementations use both other abstractions to simplify their code density and increase code reuse, and
both abstractions provide structure to the high-level, global message flows that can be productively verified.

## Slide 34: What? (field widths and return types)
Notes: By separating information about timing from policy decisions, policy designers only have to consider
current state and desired operation, yet know what general type of message needs be produced.
By eliding information about policy from the networking substrate, NoC designers know what priority channels to provision
to support any compatible policy.

## Slide 35: When? (possible and actual orderings)
Notes: TileLink transactions limit the shape of possible messages flows by declaring which ones are safe to compose.
Message flows serve as the glue that link TileLink sub-flows together based on info from local storage

## Slide 36: Which? (differentiation)

## Slide 37: All for one and one for all
Notes: Message flows choose

## Slide 38: Rocket Chip SoC generator
K. Asanović, et al. The Rocket Chip Generator. Technical Report UCB/EECS-2016-17, EECS Department, UC Berkeley, Apr 2016.
Open source
Available on github
700 commits
26 contributors
64 forks
Notes: open source, on github
external collaborators
forks

## Slide 39: Rocket Chip protocol implementations
5 policies
2 directory representations
3 manager implementations
7+ client implementations
2 NoC implementations

## Slide 40: We built some chips!
Y. Lee, et al. A 45nm 1.3ghz 16.7 Double-precision gFLOPs/W RSIC-V Processor with Vector Accelerators.
In ESSCIRC 2014-40th, pages 199–202. IEEE, 2014.
Y. Lee, et al. An Agile Approach to Building RISC-V Microprocessors.
In IEEE Micro, 35, 2015.
B. Zimmer, et al. A RISC-V Vector Processor with Tightly-Integrated Switched-Capacitor DC-DC Converters in 28nm FDSOI.
In Symposium on VLSI Circuits 2015, pages C316–C317. IEEE, 2015.
C. Sun, et al. Single-chip Microprocessor that Communicates Directly Using Light.
In Nature, 528:534–538, 2015.
Notes: Three distinct lineages (each incorporating novel device technology)
All from same source code base
All using memory hierarchy generator
From single core + htif, to multicore, to core + accel, plus L2 cache

## Slide 41: Future directions (for research)
Design space exploration using generators
  Automate building parameterized models
  Constrained and intelligent search
Formal verification and high-level specs
  Automated generation of directed tests
  Automated generation of new implementations
Application-specific protocols
  Energy consumption is the key metric
  Software memory management architecture

## Slide 42: Future directions (for me)
Notes: By bringing the power of open-source and agile hardware design to the semiconductor industry,
SiFive reduces the cost to harness the performance and energy-efficiency of customized silicon,
enabling whole new ranges of applications.

## Slide 43: Bonus storytime

## Slide 44: Bonus storytime
2007
VLS
SnbQoS
CudaDMA
ASP-GMM
RAMPGold

## Slide 45: How to graduate quickly
Focus on LPUs
  don’t build hardware
Stay single and friendless
  relationships are a distraction
Don’t piggyback travel
  don’t invite coworkers
Don’t get out
Don’t come out
Time travel to graduation

## Slide 46: Acknowledgments
Krste & Dave
  + Armando, Jonathan & Brucek
Collaborators & Barchitects
Friends & Family
Michael
Sponsors, particularly:

## Slide 47: Agile Hardware Development
Y. Lee, A. Waterman, H. Cook, B. Zimmer, A. Puggelli, J. Kwak, R. Jevtic, B. Keller, S. Bailey,
M. Blagojevic, P.-F. Chiu, R. Avizienis, B. Richards, J. Bachrach, E. Alon, B. Nikolic, and K. Asanovic.
An agile approach to building risc-v microprocessors. IEEE Micro, 35, 2015.

## Slide 48: Context-Dependent Environments

## Slide 49: CDEs: hierarchy modifications

## Slide 50: CDEs: provably robust
We can estimate the number of source code changes that will propagate through a module hierarchy given θ new parameters added

## Slide 51: Parameterizing Agents with CDEs

## Slide 52: DirectoryRepresentation API
pop(id: UInt): Remove id from the prior set of sharers.
push(id: UInt): Add id to the set of sharers.
flush(): Provide an empty set that indicates no sharers.
none(): True if there are no shared copies among this manager’s clients.
one(): True if there is a single copy at a client.
count(): Total count of the sharers among clients.
next(): Provide the id of the client that should be Probed next.
full(): Provide a full bitmap of all sharers, where a 1 indicates a copy.